## Slide 1
OpenHand
Model T42
Version 0.3
Assembly Instructions
Last updated: May 28, 2013

## Slide 2: Parts List (Flexure Base)
Part Name | Quantity | Usage | Vendor
a1.stl | 1 | Top Plate | 3D Print
a2.stl | 1 | Top Keeper Plate | 3D Print
a3.stl | 1 | Bottom Plate | 3D Print
a4.stl | 1 | Bottom Keeper Plate | 3D Print
b1.stl | 1 | Central Coupler | 3D Print
b2.stl | 2 | Servo Pulley | 3D Print
finger_flexure.stl | 2 | Finger Molds | 3D Print
Robotis RX-28 Dynamixel | 2 | Actuator | Robotis [link]
Ø1/8”, L1-1/4” steel dowel pin (J1) | 10 | Support Pin | McMaster [98381A477]
Ø3/8”, Wd1/8” nylon pulley (P1) | 6 | Tendon Routing | McMaster [3434T31]
M2.5, L5mm bolt | 2 | Fastener | Provided w/ Dynamixel McMaster [92290A055]
M2, L5mm bolt | 4 | Fastener | McMaster [91290A012]
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197]
Ø1/4”, L1-1/2” zinc-plated female standoff (S1) | 4 | Support | McMaster [93330A482]
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link]
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link]
Power Pro Spectra | 1 | Tendon | Amazon [link]
* optional

## Slide 3: Parts List (Pivot Base)
Part Name | Quantity | Usage | Vendor
a1.stl | 1 | Top Plate | 3D Print
a2.stl | 1 | Top Keeper Plate | 3D Print
a3.stl | 1 | Bottom Plate | 3D Print
a4.stl | 1 | Bottom Keeper Plate | 3D Print
b1.stl | 1 | Central Coupler | 3D Print
b2.stl | 2 | Servo Pulley | 3D Print
c1.stl | 2 | Finger Pivot Base | 3D Print
finger_pivot.stl | 2 | Finger Molds | 3D Print
Robotis RX-28 Dynamixel | 2 | Actuator | Robotis [link]
Ø1/8”, L1-1/4” steel dowel pin (J1) | 4 | Support Pin | McMaster [98381A477]
Ø1/4”, L1-3/4” steel dowel pin (J2) | 2 | Joint Pin | McMaster [98381A548]
Ø1/8”, L5/8” steel dowel pin (J3) | 6 | Support Pin | McMaster [98381A477]
Ø3/8”, Wd1/8” nylon pulley (P1) | 2 | Tendon Routing | McMaster [3434T31]
Torsion Spring, Ø0.34”, 0.028” wire diameter, 180˚, left-hand wound | 2 | Joint Return Spring | McMaster [9271K605]
M2.5, L5mm bolt | 2 | Fastener | Provided w/ Dynamixel McMaster [92290A055]
M2, L5mm bolt | 4 | Fastener | McMaster [91290A012]
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197]
Ø1/4”, L1-1/2” zinc-plated female standoff (S1) | 4 | Support | McMaster [93330A482]
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link]
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link]
Power Pro Spectra | 1 | Tendon | Amazon [link]
* optional

## Slide 4: Part Preparation
Finger Molding
Consult DDM (Dieless Deposition Manufacturing) guide for further details on pouring/preparing the joints and pads for fingers
1
finger_flexure.stl
finger_pivot.stl

## Slide 5: Part Preparation
Tendon Routing
2
Drill tendon routing holes such that tendon will run tangent to inserted pin. Minimize contact between tendon and ABS but ensure that tendon runs freely. Use helper_jig.stl to aid in positioning. Hole should be drilled perpendicular to routing surface.
Ø 1.5±0.5 mm
finger_flexure.stl (x2)
finger_pivot.stl (x2)

## Slide 6: Part Preparation
Surface Filing/Deburring
3
File down and deburr bearing surfaces as indicated above. Ensure that no support material remains, if applicable. Complementary piece (ie. pulley, finger) should slide in freely.
finger_flexure.stl (x2)
c1.stl (x2)

## Slide 7: Part Preparation
Reaming (1/8” pin holes)
4
Use Ø0.1240” reamer to prepare pin holes as indicated above. This step can be skipped in lieu of precise 3D printer calibration and parameter selection, but manual reaming is the recommended approach.
c1.stl (x2)
finger_flexure.stl (x2)
finger_pivot.stl (x2)

## Slide 8: Part Preparation
Reaming (Pivot Bases)
5
Use Ø0.2490” reamer to prepare pin holes on pivot bases c1.stl, and Ø0.2510” reamer to prepare pin holes on the corresponding fingers finger_pivot.stl. Finger should spin freely and loosely on a Ø0.25” steel pin
Ø 0.2510 “
Ø 0.2490 “
finger_pivot.stl (x2)
c1.stl (x2)

## Slide 9: Assembly
Block_actuator
6
Remove back of Dynamixel RX-28’s. The two Dynamixel servo’s snap onto the coupler piece b1.stl as shown above. Connect the two Dynamixel servos in a daisy-chain configuration.
Parts:
Dynamixel RX-28 (x2)
Dynamixel cable
b1.stl
Sunon 12VDC fan

## Slide 10: Assembly
Block_actuator
7
Assemble main drive pulleys onto actuator block sub-assembly as shown. Do not worry about zero-position of servo at this time.
(Optional): It may be beneficial to attach one end of the tendons to the pulleys at this point.
Parts:
Sub-assembly from step 6
b2.stl (x2)
M2.5, L5mm bolt (x2)
M2, L5mm bolt (x4)

## Slide 11: Assembly
Block_actuator
8
Assemble main drive pulleys onto actuator block sub-assembly as shown. Do not worry about zero-position of servo at this time.
Parts:
Sub-assembly from step 7
a3.stl
a4.stl
Ø1/4”, L1-1/2” standoffs S1 (x4)
Socket Cap Screw 8-32, L3/4” (x4)

## Slide 12: Assembly
Flexure-Base Fingers
9
For pivot-base fingers, skip to step 11. Use a shim while press-fitting the pins to help ensure that nylon pulley spins freely at finger base
Parts:
finger_flexure.stl (x2)
Pulley P1 (x6)
L1-1/4” pin J1 (x10)

## Slide 13: Assembly
Flexure-Base Fingers Top
10
Insert fingers into top plate from below as illustrated in the figures. Finger base should lie flush with plate a2.stl
Parts:
Finger sub-assembly from step 9 (x2)
a2.stl

## Slide 14: Assembly
Pivot-Base Fingers
11
Assemble pivot base sub-assembly as shown. Use shim when press-fitting the pin and pulley to ensure that the pulley spins freely after assembly.
Parts:
c1.stl (x2)
L5/8” pin J3 (x2)
Pulley P1 (x2)

## Slide 15: Assembly
Pivot-Base Fingers TOP
12
Assemble top pivot base plate as shown above. The finger pivot bases should fit flush with the top plate.
Parts:
Sub-assemblies from step 11 (x2)
a2_pivot.stl

## Slide 16: Assembly
Pivot-Base Fingers TOP
13
Assemble top pivot base plate as shown above. The finger pivot bases should fit flush with the top plate.
Parts:
Sub-assemblies from step 11 (x2)
a2_pivot.stl

## Slide 17: Assembly
14
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 8 should fit snugly
Final Assembly – Flexure base
Parts:
Bottom base sub-assembly from step 8
Top sub-assembly from step 10
a1.stl

## Slide 18: Assembly
15
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 8 should fit snugly
Final Assembly – Pivot base
Parts:
Bottom base sub-assembly from step 8
Top sub-assembly from step 13
a1.stl

## Slide 19: Tendon Routing
16
Tendons for flexure-based fingers run from the drive pulleys, through the top plate, across the 3 pulleys in the finger base, and through the finger routing ports, anchoring at the back of the fingertip, as shown above.
There should be enough tendon to leave slack after tying both ends.
Flexure-Base Fingers

## Slide 20: Tendon Routing
17
Tendons for flexure-based fingers run from the drive pulleys, through the top plate, across the pulley in the finger base, over the finger end, and through the finger routing ports, anchoring at the back of the fingertip, as shown above.
There should be enough tendon to leave slack after tying both ends.
Pivot-Base Fingers

## Slide 21: Post-Assembly
18
Servo Zero-ing
Remove the M2 bolts from the servo pulley
Loosen, but do not remove, the central M2.5 bolt, such that the servo pulley can spin freely
Connect the Dynamixel and (in position mode) move it to its zero encoder position
By hand, turn the servo pulley until the tendon between the pulley and the main drive block is as taut as possible
Re-attach the M2 bolts and tighten the servo pulley
Repeat for other servo